## Slide 1: Cache Organization

## Slide 2: Memory Hierarchy Levels
Block (aka line): unit of copying
  May be multiple words
If accessed data is present in upper level
  Hit: access satisfied by upper level
    Hit ratio: hits/accesses
If accessed data is absent
  Miss: block copied from lower level
    Time taken: miss penalty
    Miss ratio: misses/accesses = 1 – hit ratio
  Then accessed data supplied from upper level

## Slide 3: Cache Memory
Cache memory
  The level of the memory hierarchy closest to the CPU
Given accesses X1, …, Xn–1, Xn
§5.2 The Basics of Caches
How do we know if the data is present?
Where do we look?

## Slide 4: Direct Mapped Cache
Location determined by address
Direct mapped: only one choice
  (Block address) modulo (#Blocks in cache)
#Blocks is a power of 2
Use low-order address bits

## Slide 5: Tags and Valid Bits
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Actually, only need the high-order bits
  Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0

## Slide 6: Cache Example
8-blocks, 1 word/block, direct mapped
Initial state
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 7: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110

## Slide 8: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010

## Slide 9: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010

## Slide 10: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000

## Slide 11: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010

## Slide 12: Address Subdivision

## Slide 13: Example: Larger Block Size
64 blocks, 16 bytes/block
  To what block number does address 1200 map?
Block address = 1200/16 = 75
Block number = 75 modulo 64 = 11
Tag
Index
Offset
0
3
4
9
10
31
4 bits
6 bits
22 bits

## Slide 14: Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks  fewer of them
    More competition  increased miss rate
  Larger blocks  pollution
Larger miss penalty
  Can override benefit of reduced miss rate
  Early restart and critical-word-first can help

## Slide 15: Block Size Tradeoff
In general, larger block size take advantage of spatial locality BUT:
  Larger block size means larger miss penalty:
    Takes longer time to fill up the block
  If block size is too big relative to cache size, miss rate will go up
    Too few cache blocks
In general, Average Access Time:
  = Hit Time x (1 - Miss Rate) + Miss Penalty x Miss Rate
Miss
Penalty
Block Size
Miss
Rate
Exploits Spatial Locality
Fewer blocks:
compromises
temporal locality
Average
Access
Time
Increased Miss Penalty
& Miss Rate
Block Size
Block Size

## Slide 16: Extreme Example: single big line
Cache Size = 4 bytes Block Size = 4 bytes
  Only ONE entry in the cache
If an item is accessed, likely that it will be accessed again soon
  But it is unlikely that it will be accessed again immediately!!!
  The next access will likely to be a miss again
    Continually loading data into the cache but discard (force out) them before they are used again
    Worst nightmare of a cache designer: Ping Pong Effect
Conflict Misses are misses caused by:
  Different memory locations mapped to the same cache index
    Solution 1: make the cache size bigger
    Solution 2: Multiple entries for the same Cache Index
0
Cache Data
Valid Bit
Byte 0
Byte 1
Byte 3
Cache Tag
Byte 2

## Slide 17: Cache Misses
On cache hit, CPU proceeds normally
On cache miss
  Stall the CPU pipeline
  Fetch block from next level of hierarchy
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access

## Slide 18: Write-Through
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
Write through: also update memory
But makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full

## Slide 19: Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first

## Slide 20: Write Allocation
What should happen on a write miss?
Alternatives for write-through
  Allocate on miss: fetch the block
  Write around: don’t fetch the block
    Since programs often write a whole block before reading it (e.g., initialization)
For write-back
  Usually fetch the block

## Slide 21: Measuring Cache Performance
Components of CPU time
  Program execution cycles
    Includes cache hit time
  Memory stall cycles
    Mainly from cache misses
With simplifying assumptions:
§5.3 Measuring and Improving Cache Performance

## Slide 22: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2
  Load & stores are 36% of instructions
Miss cycles per instruction
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
Actual CPI = 2 + 2 + 1.44 = 5.44
  Ideal CPU is 5.44/2 =2.72 times faster

## Slide 23: Average Access Time
Hit time is also important for performance
Average memory access time (AMAT)
  AMAT = Hit time + Miss rate × Miss penalty
Example
  CPU with 1ns clock, hit time = 1 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns
    2 cycles per instruction

## Slide 24: Performance Summary
When CPU performance increased
  Miss penalty becomes more significant
Decreasing base CPI
  Greater proportion of time spent on memory stalls
Increasing clock rate
  Memory stalls account for more CPU cycles
Can’t neglect cache behavior when evaluating system performance

## Slide 25: Associative Caches
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator per entry (expensive)
n-way set associative
  Each set contains n entries
  Block number determines which set
    (Block number) modulo (#Sets in cache)
  Search all entries in a given set at once
  n comparators (less expensive)

## Slide 26: Associative Cache Example

## Slide 27: Spectrum of Associativity
For a cache with 8 entries

## Slide 28: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 

## Slide 29: Associativity Example
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 
Fully associative
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | Mem[8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 

## Slide 30: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB D-cache, 16-word blocks, SPEC2000
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 31: Set Associative Cache Organization

## Slide 32: Replacement Policy
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity

## Slide 33: Multilevel Caches
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L-2 cache misses
Some high-end systems include L-3 cache

## Slide 34: Multilevel Cache Example
Given
  CPU base CPI = 1, clock rate = 4GHz
  Miss rate/instruction = 2%
  Main memory access time = 100ns
With just primary cache
  Miss penalty = 100ns/0.25ns = 400 cycles
  Effective CPI = 1 + 0.02 × 400 = 9

## Slide 35: Example (cont.)
Now add L-2 cache
  Access time = 5ns
  Global miss rate to main memory = 0.5%
Primary miss with L-2 hit
  Penalty = 5ns/0.25ns = 20 cycles
Primary miss with L-2 miss
  Extra penalty = 420 cycles
CPI = 1 + 0.02 × 20 + 0.005 × 400 = 3.4
Performance ratio = 9/3.4 = 2.6

## Slide 36: Multilevel Cache Considerations
Primary cache
  Focus on minimal hit time
L-2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
Results
  L-1 cache usually smaller than a single cache
  L-1 block size smaller than L-2 block size

## Slide 37: Interactions with Advanced CPUs
Out-of-order CPUs can execute instructions during cache miss
  Pending store stays in load/store unit
  Dependent instructions wait in reservation stations
    Independent instructions continue
Effect of miss depends on program data flow
  Much harder to analyse
  Use system simulation

## Slide 38: The Memory Hierarchy
Common principles apply at all levels of the memory hierarchy
  Based on notions of caching
At each level in the hierarchy
  Block placement
  Finding a block
  Replacement on a miss
  Write policy
§5.5 A Common Framework for Memory Hierarchies
The BIG Picture

## Slide 39: Block Placement
Determined by associativity
  Direct mapped (1-way associative)
    One choice for placement
  n-way set associative
    n choices within a set
  Fully associative
    Any location
Higher associativity reduces miss rate
  Increases complexity, cost, and access time

## Slide 40: Finding a Block
Hardware caches
  Reduce comparisons to reduce cost
Virtual memory
  Full table lookup makes full associativity feasible
  Benefit in reduced miss rate
Associativity | Location method | Tag comparisons
Direct mapped | Index | 1
n-way set associative | Set index, then search entries within the set | n
Fully associative | Search all entries | #entries
 | Full lookup table | 0

## Slide 41: Replacement
Choice of entry to replace on a miss
  Least recently used (LRU)
    Complex and costly hardware for high associativity
  Random
    Close to LRU, easier to implement
Virtual memory
  LRU approximation with hardware support

## Slide 42: Write Policy
Write-through
  Update both upper and lower levels
  Simplifies replacement, but may require write buffer
Write-back
  Update upper level only
  Update lower level when block is replaced
  Need to keep more state
Virtual memory
  Only write-back is feasible, given disk write latency

## Slide 43: Sources of Misses
Compulsory misses (aka cold start misses)
  First access to a block
Capacity misses
  Due to finite cache size
  A replaced block is later accessed again
Conflict misses (aka collision misses)
  In a non-fully associative cache
  Due to competition for entries in a set
  Would not occur in a fully associative cache of the same total size

## Slide 44: Cache Design Trade-offs
Design change | Effect on miss rate | Negative performance effect
Increase cache size | Decrease capacity misses | May increase access time
Increase associativity | Decrease conflict misses | May increase access time
Increase block size | Decrease compulsory misses | Increases miss penalty. For very large block size, may increase miss rate due to pollution.

## Slide 45: Cache Control
Example cache characteristics
  Direct-mapped, write-back, write allocate
  Block size: 4 words (16 bytes)
  Cache size: 16 KB (1024 blocks)
  32-bit byte addresses
  Valid bit and dirty bit per block
  Blocking cache
    CPU waits until access is complete
Tag
Index
Offset
0
3
4
9
10
31
4 bits
10 bits
18 bits

## Slide 46: Interface Signals
Cache
CPU
Memory
Read/Write
Valid
Address
Write Data
Read Data
Ready
32
32
32
Read/Write
Valid
Address
Write Data
Read Data
Ready
32
128
128
Multiple cycles per access

## Slide 47: Multilevel On-Chip Caches
Per core: 32KB L1 I-cache, 32KB L1 D-cache, 512KB L2 cache
Intel Nehalem 4-core processor

## Slide 48: 3-Level Cache Organization
 | Intel Nehalem | AMD Opteron X4
L1 caches (per core) | L1 I-cache: 32KB, 64-byte blocks, 4-way, approx LRU replacement, hit time n/a L1 D-cache: 32KB, 64-byte blocks, 8-way, approx LRU replacement, write-back/allocate, hit time n/a | L1 I-cache: 32KB, 64-byte blocks, 2-way, LRU replacement, hit time 3 cycles L1 D-cache: 32KB, 64-byte blocks, 2-way, LRU replacement, write-back/allocate, hit time 3 cycles
L2 unified cache (per core) | 256KB, 64-byte blocks, 8-way, approx LRU replacement, write-back/allocate, hit time n/a | 512KB, 64-byte blocks, 16-way, approx LRU replacement, write-back/allocate, hit time 9 cycles
L3 unified cache (shared) | 8MB, 64-byte blocks, 16-way, replacement n/a, write-back/allocate, hit time n/a | 2MB, 64-byte blocks, 32-way, replace block shared by fewest cores, write-back/allocate, hit time 38 cycles
n/a: data not available |  | 

## Slide 49: Way Prediction
To improve hit time, predict the way to pre-set mux
  Mis-prediction gives longer hit time
  Prediction accuracy
    > 90% for two-way
    > 80% for four-way
    I-cache has better accuracy than D-cache
  First used on MIPS R10000 in mid-90s
  Used on ARM Cortex-A8
Extend to predict block as well
  “Way selection”
  Increases mis-prediction penalty
Advanced Optimizations

## Slide 50: Pipelining Cache
Pipeline cache access to improve bandwidth
  Examples:
    Pentium: 1 cycle
    Pentium Pro – Pentium III: 2 cycles
    Pentium 4 – Core i7: 4 cycles
Increases branch mis-prediction penalty
Makes it easier to increase associativity
Advanced Optimizations

## Slide 51: Nonblocking Caches
Allow hits before previous misses complete
  “Hit under miss”
  “Hit under multiple miss”
L2 must support this
In general, processors can hide L1 miss penalty but not L2 miss penalty
Advanced Optimizations

## Slide 52: Multibanked Caches
Organize cache as independent banks to support simultaneous access
  ARM Cortex-A8 supports 1-4 banks for L2
  Intel i7 supports 4 banks for L1 and 8 banks for L2
Interleave banks according to block address
Advanced Optimizations

## Slide 53: Critical Word First, Early Restart
Critical word first
  Request missed word from memory first
  Send it to the processor as soon as it arrives
Early restart
  Request words in normal order
  Send missed work to the processor as soon as it arrives
Effectiveness of these strategies depends on block size and likelihood of another access to the portion of the block that has not yet been fetched
Advanced Optimizations

## Slide 54: Merging Write Buffer
When storing to a block that is already pending in the write buffer, update write buffer
Reduces stalls due to full write buffer
Do not apply to I/O addresses
Advanced Optimizations
No write buffering
Write buffering

## Slide 55: Compiler Optimizations
Loop Interchange
  Swap nested loops to access memory in sequential order
Blocking
  Instead of accessing entire rows or columns, subdivide matrices into blocks
  Requires more memory accesses but improves locality of accesses
Advanced Optimizations

## Slide 56: Hardware Prefetching
Fetch two blocks on miss (include next sequential block)
Advanced Optimizations
Pentium 4 Pre-fetching

## Slide 57: Compiler Prefetching
Insert prefetch instructions before data is needed
Non-faulting: prefetch doesn’t cause exceptions
Register prefetch
  Loads data into register
Cache prefetch
  Loads data into cache
Combine with loop unrolling and software pipelining
Advanced Optimizations

## Slide 58: Summary
Advanced Optimizations

## Slide 59: Concluding Remarks
Fast memories are small, large memories are slow
  We really want fast, large memories 
  Caching gives this illusion 
Principle of locality
  Programs use a small part of their memory space frequently
Memory hierarchy
  L1 cache  L2 cache  …  DRAM memory  disk
Memory system design is critical for multiprocessors