## Slide 1: Multithreaded Processors

## Slide 2: Multithreading
Performing multiple threads of execution in parallel
  Replicate registers, PC, etc.
  Fast switching between threads
Fine-grain multithreading
  Switch threads after each cycle
  Interleave instruction execution
  If one thread stalls, others are executed
Coarse-grain multithreading
  Only switch on long stall (e.g., L2-cache miss)
  Simplifies hardware, but doesn’t hide short stalls (eg, data hazards)

## Slide 3: Simultaneous Multithreading
In superscalar dynamically scheduled processor
  Schedule instructions from multiple threads
  Instructions from independent threads execute when function units are available
  Within threads, dependencies handled by scheduling and register renaming
Examples:
  Intel Xeon with Hyperthreading. Two threads: duplicated registers, shared function units and caches
  IBM Power – 4 threads.

## Slide 4: Multithreading Example

## Slide 5: The SMT Datapath
Instruction
Cache
Fetch
Unit
PC
PC
PC
PC
Decode
Register Rename
Issue Queue
Load/Store
Queues
Register
File
PC
PC
PC
Execution
Units
Data
Cache
PC
LDST
Units
Re-order Buffers
Private Resources
Shared Resources
Arch State

## Slide 6: SMT Key Design Issues
Preventing one thread from hogging the shared datapath resources, and thus denying them to the instructions from other threads
Previous techniques address this in one of two ways:
  Indirectly via the use of various fetching policies
  Directly via static partitioning of datapath resources, rather than complete sharing.

## Slide 7: Future of Multithreading
Will it survive? In what form?
Power considerations  simplified microarchitectures
  Simpler forms of multithreading
Tolerating cache-miss latency
  Thread switch may be most effective
Multiple simple cores might share resources more effectively